## Slide 1: Computer Architecture
Chapter 4 - Register Transfer and Micro Operations
Part 1

## Slide 2: REGISTER TRANSFER AND MICROOPERATIONS
• Register Transfer Language
• Register Transfer
• Bus and Memory Transfers
• Arithmetic Microoperations
• Logic Microoperations
• Shift Microoperations
• Arithmetic Logic Shift Unit

## Slide 3: SIMPLE DIGITAL SYSTEMS
Combinational and sequential circuits can be used to create simple digital systems.
These are the low-level building blocks of a digital computer.
Simple digital systems are frequently characterized in terms of
  the registers they contain, and
  the operations that they perform.
Typically,
  What operations are performed on the data in the registers
  What information is passed between registers

## Slide 4: MICROOPERATIONS (1)
Register Transfer Language
The operations on the data in registers are called microoperations.
The functions built into registers are examples of microoperations
  Shift
  Load
  Clear
  Increment
  …

## Slide 5: MICROOPERATION (2)
An elementary operation performed (during
one clock pulse), on the information stored
in one or more registers
R  f(R, R)
f: shift, load, clear, increment, add, subtract, complement,
and, or, xor, …
ALU
(f)
Registers
(R)
1 clock cycle
Register Transfer Language

## Slide 6: ORGANIZATION OF A DIGITAL SYSTEM
- Set of registers and their functions
- Microoperations set
Set of allowable microoperations provided
by the organization of the computer
- Control signals that initiate the sequence of
microoperations (to perform the functions)
Definition of the (internal) organization of a computer
Register Transfer Language

## Slide 7: REGISTER TRANSFER LEVEL
Register Transfer Language
Viewing a computer, or any digital system, in this way is called the register transfer level
This is because we’re focusing on
  The system’s registers
  The data transformations in them, and
  The data transfers between them.

## Slide 8: REGISTER TRANSFER LANGUAGE
Register Transfer Language
Rather than specifying a digital system in words, a specific notation is used, register transfer language
For any function of the computer, the register transfer language can be used to describe the (sequence of) micro-operations
Register transfer language
  A symbolic language
  A convenient tool for describing the internal organization of digital computers
  Can also be used to facilitate the design process of digital systems.

## Slide 9: DESIGNATION OF REGISTERS
Register Transfer Language
Registers are designated by capital letters, sometimes followed by numbers (e.g., A, R13, IR)
Often the names indicate function:
  MAR - memory address register
  PC - program counter
  IR - instruction register
Registers and their contents can be viewed and represented in various ways
  A register can be viewed as a single entity:
  Registers may also be represented showing the bits of data they contain
MAR

## Slide 10: DESIGNATION OF REGISTERS
Register Transfer Language
R1
Register
Numbering of bits
Showing individual bits
Subfields
PC(H)
PC(L)
15
8
7
0
- a register
- portion of a register
- a bit of a register
Common ways of drawing the block diagram of a register
7 6 5 4 3 2 1 0
R2
15
0
Designation of a register

## Slide 11: REGISTER TRANSFER
Register Transfer
Copying the contents of one register to another is a register transfer
A register transfer is indicated as
  R2  R1
  In this case the contents of register R1 are copied (loaded) into register R2
  A simultaneous transfer of all bits from the source R1 to the destination register R2, during one clock pulse
  Note that this is a non-destructive; i.e. the contents of R1 are not altered by copying (loading) them to R2

## Slide 12: REGISTER TRANSFER
Register Transfer
A register transfer such as
  R3  R5
  Implies that the digital system has
  the data lines from the source register (R5) to the destination register (R3)
  Parallel load in the destination register (R3)
  Control lines to perform the action

## Slide 13: CONTROL FUNCTIONS
Register Transfer
Often actions need to only occur if a certain condition is true
This is similar to an “if” statement in a programming language
In digital systems, this is often done via a control signal, called a control function
  If the signal is 1, the action takes place
This is represented as:
  P: R2  R1
  Which means “if P = 1, then load the contents of register R1 into register R2”, i.e., if (P = 1) then (R2  R1)

## Slide 14: HARDWARE IMPLEMENTATION OF CONTROLLED TRANSFERS
Implementation of controlled transfer
P: R2 R1
Block diagram
Timing diagram
Clock
Register Transfer
Transfer occurs here
R2
R1
Control
Circuit
Load
P
n
Clock
Load
t
t+1
The same clock controls the circuits that generate the control function
and the destination register
Registers are assumed to use positive-edge-triggered flip-flops

## Slide 15: SIMULTANEOUS OPERATIONS
Register Transfer
If two or more operations are to occur simultaneously, they are separated with commas
  P: R3  R5, MAR  IR
Here, if the control function P = 1, load the contents of R5 into R3, and at the same time (clock), load the contents of register IR into register MAR

## Slide 16: BASIC SYMBOLS FOR REGISTER TRANSFERS
Capital letters Denotes a register MAR, R2
& numerals
Parentheses () Denotes a part of a register R2(0-7), R2(L)
Arrow  Denotes transfer of information R2  R1
Colon : Denotes termination of control function P:
Comma , Separates two micro-operations A  B, B  A
Symbols
Description Examples
Register Transfer

## Slide 17: CONNECTING REGISTRS
Register Transfer
In a digital system with many registers, it is impractical to have data and control lines to directly allow each register to be loaded with the contents of every possible other registers
To completely connect n registers  n(n-1) lines
O(n2) cost
  This is not a realistic approach to use in a large digital system
Instead, take a different approach
Have one centralized set of circuits for data transfer – the bus
Have control circuits to select which register is the source, and which is the destination

## Slide 18: BUS AND BUS TRANSFER
Bus is a path(of a group of wires) over which information is transferred, from any of several sources to any of several destinations.
From a register to bus: BUS  R
1
2
3
4
1
2
3
4
1
2
3
4
1
2
3
4
Register A
Register B
Register C
Register D
B
C
D
1
1
1
4 x1
MUX
B
C
D
2
2
2
4 x1
MUX
B
C
D
3
3
3
4 x1
MUX
B
C
D
4
4
4
4 x1
MUX
4-line bus
x
y
select
0
0
0
0
Register A
Register B
Register C
Register D
Bus lines
Bus and Memory Transfers

## Slide 19: TRANSFER FROM BUS TO A DESTINATION REGISTER
Reg. R0
Reg. R1
Reg. R2
Reg. R3
Bus lines
2 x 4
Decoder
Load
D
0
D
1
D
2
D
3
z
w
Select
E (enable)
Bus and Memory Transfers

## Slide 20: BUS TRANSFER IN RTL
Bus and Memory Transfers
Depending on whether the bus is to be mentioned explicitly or not, register transfer can be indicated as either
or
In the former case the bus is implicit, but in the latter, it is explicitly indicated
R2 R1
BUS R1, R2  BUS

## Slide 21: MEMORY (RAM)
Bus and Memory Transfers
Memory (RAM) can be thought as a sequential circuits containing some number of registers
These registers hold the words of memory
Each of the r registers is indicated by an address
These addresses range from 0 to r-1
Each register (word) can hold n bits of data
Assume the RAM contains r = 2k words. It needs the following
  n data input lines
  n data output lines
  k address lines
  A Read control line
  A Write control line
data input lines
data output lines
n
n
k
address lines
Read
Write
RAM
unit

## Slide 22: MEMORY TRANSFER
Bus and Memory Transfers
Collectively, the memory is viewed at the register level as a device, M.
Since it contains multiple locations, we must specify which address in memory we will be using
This is done by indexing memory references
Memory is usually accessed in computer systems by putting the desired address in a special register, the Memory Address Register (MAR, or AR)
When memory is accessed, the contents of the MAR get sent to the memory unit’s address lines
AR
Memory
unit
Read
Write
Data in
Data out
M

## Slide 23: MEMORY READ
Bus and Memory Transfers
To read a value from a location in memory and load it into a register, the register transfer language notation looks like this:
This causes the following to occur
  The contents of the MAR get sent to the memory address lines
  A Read (= 1) gets sent to the memory unit
  The contents of the specified address are put on the memory’s output data lines
  These get sent over the bus to be loaded into register R1
R1  M[MAR]

## Slide 24: MEMORY WRITE
Bus and Memory Transfers
To write a value from a register to a location in memory looks like this in register transfer language:
This causes the following to occur
  The contents of the MAR get sent to the memory address lines
  A Write (= 1) gets sent to the memory unit
  The values in register R1 get sent over the bus to the data input lines of the memory
  The values get loaded into the specified address in the memory
M[MAR]  R1

## Slide 25: SUMMARY OF R. TRANSFER MICROOPERATIONS
Bus and Memory Transfers
A  B Transfer content of reg. B into reg. A
AR DR(AD) Transfer content of AD portion of reg. DR into reg. AR
A  constant Transfer a binary constant into reg. A
ABUS  R1, Transfer content of R1 into bus A and, at the same time,
R2 ABUS transfer content of bus A into R2
AR Address register
DR Data register
M[R] Memory word specified by reg. R
M Equivalent to M[AR]
DR  M Memory read operation: transfers content of
memory word specified by AR into DR
M  DR Memory write operation: transfers content of
DR into memory word specified by AR