## Slide 1: Data Communication and Computer Networking

## Slide 2: Data Communication and Computer Networking
2
Dr. Hany Soliman Elnashar
PhD., PMP., ITIL., and TOGAF.
Computer Engineering And Systems Builder
Email: nhany73s@gmail.com

## Slide 3: Textbooks
 | Degrees
20 | Midterm
10 | Quiz’s
10 | sec
10 | Others

## Slide 5: Chapter 1

## Slide 6: Data and Computer Communications
Data Communications
Networking
Protocols
Computer communication: the exchange of information (signals)
between 2 or more computers
Computer Network: technology and architecture that allow 2 or more computers are interconnected via a communication network
Protocols: Set of procedures used for communications between entities in different systems

## Slide 7: A Communications Model
Source: generates data to be transmitted (telephone, PC)
Transmitter (modems) : Converts data into transmittable signals.
Transmission System: Can be single line or complex network system
Receiver : Converts received signal into data (modems)
Destination : Takes incoming data (telephone, PC)

## Slide 8: Simplified Data Communications Model

## Slide 9: 1- Communications Topics (Tasks)
Transmission System Utilization
Interfacing
Signal Generation
Synchronization
Exchange Management
Error detection and correction
Addressing and routing
Recovery
Message formatting
Security
Network Management

## Slide 10: Transmission Mode
Simplex
  Unidirectional
  As one-way street
Half-duplex
  Transmit and receive are possible, but not at the same time
  Like a one-lane road with two-directional traffic
Full-duplex
  Transmit and receive simultaneously
  Like a two-way street, telephone network
  Channel capacity must be divided between two directions
Simplex
Half-Duplex
Full-Duplex

## Slide 11: 2- Network
Topology: the geometric arrangement of devices on the
network.
Protocols: the rules and encoding specifications for
sending and receiving Data
Media: Devices can be connected by coaxial cables, fiber optics or wireless via radio waves
Medium Access control: schema allow sharing of the media
Characteristics differentiate one Network from another
Network: A set of computers and equipments (nodes) connected by communication links
Enterprise Network : 2 or more LANs connected to each other or one LAN connected to WAN
File Server: a computer that contain files shared by PCs on a network
Intranet: a private version of the internet

## Slide 12
Criteria of Efficient network System
performance
Response time For 1- transmission
2- Data processing
Throughput
Amount of work performed by system / time
Reliability
Measure of system Failure (mean time between failure)
Fault- tolerance solution
Design - Duplication
Consistency
Same thing all time
Response time
Flexibility
Growth change is available with minimum impact on users
Legacy system
Standard help

## Slide 14: Network Essentials
Technologies
Models
Types
Physical
Topologies
- Ethernet
Token ring
Transmission control
Protocol/internet
Protocol TCP/IP
Wireless application
Client/server
Peer-to-peer
LAN
MAN
WAN
Intranet
internet
Bus
Ring
Star

## Slide 15: Network Line configuration
Point-to-point
  Dedicated link between two devices
  The entire capacity of the channel is reserved
  Examples: Microwave link, TV remote control
Multipoint
  More than two devices share a single link
  Capacity of the channel is either
    shared: Devices can use the link simultaneously
    Timeshare: Users take turns

## Slide 16: Network Models
Client/server Model:
Microcomputer users or
clients share services of
a centralized computer
called server
Peer-to-peer
Computers share equally with one another without having to rely on a central server
server

## Slide 17: Physical Topology
The topology of a network is the geometric representation of the relationship of all the links and linking devices (nodes) to one another.
There are four basic topologies : mesh, star, bus, and ring
1- Mesh Topology
Every device has a dedicated link to every other device.
Number of physical links in mesh with n nodes. Each connected to n – 1 nodes = n(n - 1) physical links
if each physical link allows communication in both directions (duplex mode) the number of links by 2. so, we need n(n -1) /2

## Slide 18: 3- Bus Topology
2- star Topology
Each device needs only one link and one I/O port to connect it to any number of others. This factor also makes it easy to install and reconfigure.
Nodes connected to the bus cable by drop lines and taps.
Advantages of a bus topology: ease of installation.
Disadvantages :difficult reconnection

## Slide 19
4- ring Topology
Each device has dedicated point-to - point connection with only the two devices on either side of it.
signal is passed along the ring in one direction until reaches its destination.
Each device in ring incorporates a repeater. When a device receives a signal intended for another device, its repeater regenerates the bits and passes them
Repeater
Repeater
4- Tree Topology

## Slide 20: Types of Networks
1- Local Area Networks
Building or small campus
from 10m up to 1 km
Data rates much higher
Usually broadcast systems
Now some switched systems and ATM are being introduced

## Slide 21
2- Man : It is suitable for
Large geographical area
Crossing public rights of way
Up to 10km (city)
3-WAN
-from 100 km up to 1000km

## Slide 22
Internetwork (Internet)
up to 10000km

## Slide 23
Assume we need to download text documents at the rate of 100 pages per minute. What is the required bit rate of the channel?
Solution
A page is an average of 24 lines with 80 characters in each line. If we assume that one character requires 8 bits, the bit rate is

## Slide 24
L3: Switching Networks for WAN
  Circuit–switching
  Network
  Packet- switching
  Network
  Message-witched
  Network
  Datagram Network
  Virtual-circuit
  Networks

## Slide 25: Circuit Switching
Made of a set of switches connected by physical links, in which each link is divided into n channels
e.g. telephone network
One link
n channel
Packet Switching
No resources reservation, resources are allocated based on demand

## Slide 26: Integrated Services Digital Network -ISDN
Designed to replace public telecom system
Introduce a Wide variety of services (telephone, video on demand VoD, digital data)
Entirely digital domain
Narrowband ISDN
use 64 kb/s channel as basic switching unite
used with circuit switching
Broadband ISDN
very high data rate up to 100s Mb/s
used with packet switching

## Slide 27: Logical and physical connection
Logical connection: exists only in the software
physical connection: exists in the hardware
One link
n channel
Network architecture
Logical connection:
All higher Layers
physical connection:
exists in the physical Layer only

## Slide 28: What are Switched Networks?
Switched Network
Switch: moves bits between links
  Packet switching
  Circuit switching

## Slide 29: Back in the Old Days…

## Slide 30: Then Came TDM…
Multiplex (mux)
Demultiplex (demux)
Synchronous time division multiplexing

## Slide 31: TDM Logical Network View

## Slide 32: Packet Switching (Internet)
Packets

## Slide 33: Packet Switching
Interleave packets from different sources
Efficient: resources used on demand
  Statistical multiplexing
General
  Multiple types of applications
Accommodates bursty traffic
  Addition of queues

## Slide 34: Statistical Multiplexing Gain
1 Mbps link; users require 0.1 Mbps when transmitting; users active only 10% of the time
Circuit switching: can support 10 users
Packet switching: with 35 users, probability that >=10 are transmitting at the same time < 0.0017
Notes: 1-SUM[from n=0..9 of (35 chose n) * (.1^n) * (1-.1)^(40-n)

## Slide 35: Characteristics of Packet Switching
Store and forward
  Packets are self contained units
  Can use alternate paths – reordering
Contention
  Congestion
  Delay

## Slide 36: Second Step: Internet[work]
Internet[work]
A collection of interconnected networks
Host: network endpoints (computer, PDA, light switch, …)
Router: node that connects networks
Internet vs. internet
Notes: What if want to communicate between hosts on different Ethernets? Internet as interoperability layer

## Slide 37: Challenge
Many differences between networks
  Address formats
  Performance – bandwidth/latency
  Packet size
  Loss rate/pattern/handling
  Routing
How to translate between various network technologies

## Slide 38: Third Step: How To Find Nodes?
Internet
Computer 1
Computer 2

## Slide 39: Naming
Humans use readable host names
  E.g. www.cmu.edu
  Globally unique (can correspond to multiple hosts)
Naming system translates to physical address
  E.g. DNS translates name to IP Address (e.g. 128.2.11.43)
  Address reflects location in network

## Slide 40: Domain Name System
What’s the IP address for www.cmu.edu?
It is 128.2.11.43
DNS server address manually configured into OS
Local DNS Server
Computer 1

## Slide 41: Packet Routing/Delivery
Each network technology has different local delivery methods
Address resolution provides delivery information within network
  E.g., ARP maps IP addresses to Ethernet addresses
  Local, works only on a particular network
Routing protocol provides path through an internetwork

## Slide 42: Network:Address Resolution Protocol
Ethernet
Broadcast: who knows the
Ethernet address for 128.2.11.43?
Ethernet
Unicast: Yes, it is
08-00-2c-19-dc-45

## Slide 43: Internetwork: Datagram Routing
R
R
R
R
R
H
H
H
H
R
R
H
R
Routers send packet to next closest point
H: Hosts
R: Routers

## Slide 44: Routing
Forwarding tables at each router populated by routing protocols.
Original Internet: manually updated
Routing protocols update tables based on “cost”
  Exchange tables with neighbors or everyone
  Use neighbor leading to shortest path

## Slide 45: Fourth Step: Application Demands
Reliability
  Corruption
  Lost packets
Flow and congestion control
Fragmentation
In-order delivery
Etc…

## Slide 46: What if the Data gets Corrupted?
Internet
GET windex.html
GET index.html
Solution: Add a checksum
Problem: Data Corruption
0,9
9
6,7,8
21
4,5
7
1,2,3
6
X

## Slide 47: What if Network is Overloaded?
Problem: Network Overload
Short bursts: buffer
What if buffer overflows?
  Packets dropped
  Sender adjusts rate until load = resources
Called “congestion control”
Solution: Buffering and Congestion Control

## Slide 48: What if the Data gets Lost?
Internet
GET index.html
Problem: Lost Data
Internet
GET index.html
Solution: Timeout and Retransmit
GET index.html
GET index.html

## Slide 49: What if the Data Doesn’t Fit?
Problem: Packet size
Solution: Fragment data across packets
On Ethernet, max IP packet is 1.5kbytes
Typical web page is 10kbytes
GET
inde
x.ht
ml
GET index.html

## Slide 50: What if the Data is Out of Order?
Solution: Add Sequence Numbers
Problem: Out of Order
GET
x.ht
inde
ml
GET x.htindeml
GET index.html
ml
4
inde
2
x.ht
3
GET
1

## Slide 51: Network Functionality Summary
Link
Multiplexing
Routing
Addressing/naming (locating peers)
Reliability
Flow control
Fragmentation
Etc….

## Slide 52
SHEET
  PAGE 24-25