## Slide 1: PROGRAMMING THE BASIC COMPUTER
Introduction
Machine Language
Assembly Language
Assembler
Program Loops
Programming Arithmetic and Logic Operations
Subroutines
Input-Output Programming

## Slide 2: INTRODUCTION
Symbol
Hexa code
Description
Those concerned with computer architecture should
have a knowledge of both hardware and software
because the two branches influence each other.
m: effective address
M: memory word (operand)
found at m
Introduction
  AND 0 or 8 AND M to AC
  ADD 1 or 9 Add M to AC, carry to E
  LDA 2 or A Load AC from M
  STA 3 or B Store AC in M
  BUN 4 or C Branch unconditionally to m
  BSA 5 or D Save return address in m and branch to m+1
  ISZ 6 or E Increment M and skip if zero
  CLA 7800 Clear AC
  CLE 7400 Clear E
  CMA 7200 Complement AC
  CME 7100 Complement E
  CIR 7080 Circulate right E and AC
  CIL 7040 Circulate left E and AC
  INC 7020 Increment AC, carry to E
  SPA 7010 Skip if AC is positive
  SNA 7008 Skip if AC is negative
  SZA 7004 Skip if AC is zero
  SZE 7002 Skip if E is zero
  HLT 7001 Halt computer
  INP F800 Input information and clear flag
  OUT F400 Output information and clear flag
  SKI F200 Skip if input flag is on
  SKO F100 Skip if output flag is on
  ION F080 Turn interrupt on
  IOF F040 Turn interrupt off
Instruction Set of the Basic Computer

## Slide 3: MACHINE LANGUAGE
Program
A list of instructions or statements for directing
the computer to perform a required data
processing task
Various types of programming languages
- Hierarchy of programming languages
    Machine-language
- Binary code
- Octal or hexadecimal code
    Assembly-language (Assembler)
- Symbolic code
    High-level language (Compiler)
Machine Language

## Slide 4: COMPARISON OF PROGRAMMING LANGUAGES
0 0010 0000 0000 0100
1 0001 0000 0000 0101
10 0011 0000 0000 0110
11 0111 0000 0000 0001
100 0000 0000 0101 0011
101 1111 1111 1110 1001
110 0000 0000 0000 0000
Binary Program to Add Two Numbers
Location Instruction Code
000 2004
001 1005
002 3006
003 7001
004 0053
005 FFE9
006 0000
Hexa program
Location Instruction
Program with Symbolic OP-Code
000 LDA 004 Load 1st operand into AC
001 ADD 005 Add 2nd operand to AC
002 STA 006 Store sum in location 006
003 HLT Halt computer
004 0053 1st operand
005 FFE9 2nd operand (negative)
006 0000 Store sum here
Location Instruction Comments
Assembly-Language Program
Fortran Program
INTEGER A, B, C
DATA A,83 / B,-23
C = A + B
END
Machine Language
  ORG 0 /Origin of program is location 0
  LDA A /Load operand from location A
  ADD B /Add operand from location B
  STA C /Store sum in location C
  HLT /Halt computer
  A, DEC 83 /Decimal operand
  B, DEC -23 /Decimal operand
  C, DEC 0 /Sum stored in location C
  END /End of symbolic program

## Slide 5: ASSEMBLY LANGUAGE
Syntax of the BC assembly language
Each line is arranged in three columns called fields
Label field
- May be empty or may specify a symbolic
address consists of up to 3 characters
- Terminated by a comma
Instruction field
- Specifies a machine or a pseudo instruction
- May specify one of
* Memory reference instr. (MRI)
MRI consists of two or three symbols separated by spaces.
ADD OPR (direct address MRI)
ADD PTR I (indirect address MRI)
* Register reference or input-output instr.
Non-MRI does not have an address part
* Pseudo instr. with or without an operand
Symbolic address used in the instruction field must be
defined somewhere as a label
Comment field
- May be empty or may include a comment
  Assembly Language

## Slide 6: PSEUDO-INSTRUCTIONS
  ORG N
  Hexadecimal number N is the memory loc.
  for the instruction or operand listed in the following line
  END
  Denotes the end of symbolic program
  DEC N
  Signed decimal number N to be converted to the binary
  HEX N
  Hexadecimal number N to be converted to the binary
Example: Assembly language program to subtract two numbers
ORG 100
LDA SUB
CMA
INC
ADD MIN
STA DIF
HLT
DEC 83
DEC -23
HEX 0
END
/ Origin of program is location 100
/ Load subtrahend to AC
/ Complement AC
/ Increment AC
/ Add minuend to AC
/ Store difference
/ Halt computer
/ Minuend
/ Subtrahend
/ Difference stored here
/ End of symbolic program
MIN,
SUB,
DIF,
  Assembly Language

## Slide 7: TRANSLATION TO BINARY
ORG 100
LDA SUB
CMA
INC
ADD MIN
STA DIF
HLT
DEC 83
DEC -23
HEX 0
END
MIN,
SUB,
DIF,
100 2107
101 7200
102 7020
103 1106
104 3108
105 7001
106 0053
107 FFE9
108 0000
Symbolic Program
Location Content
Hexadecimal Code
  Assembly Language

## Slide 8: ASSEMBLER - FIRST PASS -
Assembler
Source Program - Symbolic Assembly Language Program
Object Program - Binary Machine Language Program
Two pass assembler
1st pass: generates a table that correlates all user defined
(address) symbols with their binary equivalent value
2nd pass: binary translation
First pass
Assembler
First pass
LC := 0
Scan next line of code
Set LC
Label
no
yes
yes
no
ORG
Store symbol
in address-
symbol table
together with
value of LC
END
Increment LC
Go to
second
pass
no
yes

## Slide 9: ASSEMBLER - SECOND PASS -
Machine instructions are translated by means of table-lookup procedures;
(1. Pseudo-Instruction Table, 2. MRI Table, 3. Non-MRI Table
4. Address Symbol Table)
Assembler
Second pass
LC <- 0
Scan next line of code
Set LC
yes
yes
ORG
Pseudo
instr.
yes
END
no
Done
yes
MRI
no
Valid
non-MRI
instr.
no
Convert
operand
to binary
and store
in location
given by LC
no
DEC or
HEX
Error in
line of
code
Store binary
equivalent of
instruction
in location
given by LC
yes
no
Get operation code
and set bits 12-14
Search address-
symbol table for
binary equivalent
of symbol address
and set bits 0-11
I
Set
first
bit to 0
Set
first
bit to 1
yes
no
Assemble all parts of
binary instruction and
store in location given by LC
Increment LC
Second Pass

## Slide 10: PROGRAM LOOPS
DIMENSION A(100)
INTEGER SUM, A
SUM = 0
DO 3 J = 1, 100
SUM = SUM + A(J)
3
ORG 100
LDA ADS
STA PTR
LDA NBR
STA CTR
CLA
ADD PTR I
ISZ PTR
ISZ CTR
BUN LOP
STA SUM
HLT
HEX 150
HEX 0
DEC -100
HEX 0
HEX 0
ORG 150
DEC 75
DEC 23
END
/ Origin of program is HEX 100
/ Load first address of operand
/ Store in pointer
/ Load -100
/ Store in counter
/ Clear AC
/ Add an operand to AC
/ Increment pointer
/ Increment counter
/ Repeat loop again
/ Store sum
/ Halt
/ First address of operands
/ Reserved for a pointer
/ Initial value for a counter
/ Reserved for a counter
/ Sum is stored here
/ Origin of operands is HEX 150
/ First operand
/ Last operand
/ End of symbolic program
LOP,
ADS,
PTR,
NBR,
CTR,
SUM,
Program Loops
Loop: A sequence of instructions that are executed many times,
each with a different set of data
Fortran program to add 100 numbers:
.
.
.
Assembly-language program to add 100 numbers: