## Slide 1: PROGRAMMING ARITHMETIC AND LOGIC OPERATIONS
- Software Implementation
- Implementation of an operation with a program
using machine instruction set
- Usually when the operation is not included
in the instruction set
- Hardware Implementation
- Implementation of an operation in a computer
with one machine instruction
Software Implementation example:
* Multiplication
- For simplicity, unsigned positive numbers
- 8-bit numbers -> 16-bit product
Programming Arithmetic and Logic Operations
Implementation of Arithmetic and Logic Operations

## Slide 2: FLOWCHART OF A PROGRAM - Multiplication -
X holds the multiplicand
Y holds the multiplier
P holds the product
Example with four significant digits
0000 1111
0000 1011 0000 0000
0000 1111 0000 1111
0001 1110 0010 1101
0000 0000 0010 1101
0111 1000 1010 0101
1010 0101
Programming Arithmetic and Logic Operations
cil
CTR  - 8
P  0
E  0
AC  Y
Y  AC
cir EAC
E
P  P + X
E  0
AC  X
cil EAC
X  AC
CTR  CTR + 1
=1
=0
CTR
=0
Stop
 0
X =
Y =
P

## Slide 3: ASSEMBLY LANGUAGE PROGRAM - Multiplication -
ORG 100
CLE
LDA Y
CIR
STA Y
SZE
BUN ONE
BUN ZRO
LDA X
ADD P
STA P
CLE
LDA X
CIL
STA X
ISZ CTR
BUN LOP
HLT
DEC -8
HEX 000F
HEX 000B
HEX 0
END
/ Clear E
/ Load multiplier
/ Transfer multiplier bit to E
/ Store shifted multiplier
/ Check if bit is zero
/ Bit is one; goto ONE
/ Bit is zero; goto ZRO
/ Load multiplicand
/ Add to partial product
/ Store partial product
/ Clear E
/ Load multiplicand
/ Shift left
/ Store shifted multiplicand
/ Increment counter
/ Counter not zero; repeat loop
/ Counter is zero; halt
/ This location serves as a counter
/ Multiplicand stored here
/ Multiplier stored here
/ Product formed here
LOP,
ONE,
ZRO,
CTR,
X,
Y,
P,
Programming Arithmetic and Logic Operations

## Slide 4: ASSEMBLY LANGUAGE PROGRAM - Logic and Shift Operations -
Logic operations
- BC instructions : AND, CMA, CLA
- Program for OR operation (A+B) = (A\B\)\
LDA A
CMA
STA TMP
LDA B
CMA
AND TMP
CMA
/ Load 1st operand
/ Complement to get A’
/ Store in a temporary location
/ Load 2nd operand B
/ Complement to get B’
/ AND with A’ to get A’ AND B’
/ Complement again to get A OR B
Shift operations - BC has Circular Shift only
- Logical shift-right operation - Logical shift-left operation
CLE CLE
CIR CIL
- Arithmetic right-shift operation
CLE
SPA
CME
CIR
/ Clear E to 0
/ Skip if AC is positive
/ AC is negative
/ Circulate E and AC
Programming Arithmetic and Logic Operations

## Slide 5: SUBROUTINES
- A set of common instructions that can be used in a program many times.
- Subroutine linkage : a procedure for branching
to a subroutine and returning to the main program
ORG 100
LDA X
BSA SH4
STA X
LDA Y
BSA SH4
STA Y
HLT
HEX 1234
HEX 4321
HEX 0
CIL
CIL
CIL
CIL
AND MSK
BUN SH4 I
HEX FFF0
END
/ Main program
/ Load X
/ Branch to subroutine
/ Store shifted number
/ Load Y
/ Branch to subroutine again
/ Store shifted number
/ Subroutine to shift left 4 times
/ Store return address here
/ Circulate left once
/ Circulate left fourth time
/ Set AC(0-3) to zero
/ Return to main program
/ Mask operand
X,
Y,
SH4,
MSK,
100
101
102
103
104
105
106
107
108
109
10A
10B
10C
10D
10E
10F
110
Loc.
Subroutines
Subroutine
Example : Sub Routine that makes Logical Shift Left 4 times

## Slide 6: SUBROUTINE PARAMETERS AND DATA LINKAGE
ORG 200
LDA X
BSA OR
HEX 3AF6
STA Y
HLT
HEX 7B95
HEX 0
HEX 0
CMA
STA TMP
LDA OR I
CMA
AND TMP
CMA
ISZ OR
BUN OR I
HEX 0
END
/ Load 1st operand into AC
/ Branch to subroutine OR
/ 2nd operand stored here
/ Subroutine returns here
/ 1st operand stored here
/ Result stored here
/ Subroutine OR
/ Complement 1st operand
/ Store in temporary location
/ Load 2nd operand
/ Complement 2nd operand
/ AND complemented 1st operand
/ Complement again to get OR
/ Increment return address
/ Return to main program
/ Temporary storage
X,
Y,
OR,
TMP,
200
201
202
203
204
205
206
207
208
209
20A
20B
20C
20D
20E
20F
210
Loc.
Example: Subroutine performing LOGICAL OR operation; Need two parameters
Subroutines
Linkage of Parameters and Data between the Main Program and a Subroutine
- via Registers
- via Memory locations
- ….

## Slide 7: SUBROUTINE - Moving a Block of Data -
BSA MVE
HEX 100
HEX 200
DEC -16
HLT
HEX 0
LDA MVE I
STA PT1
ISZ MVE
LDA MVE I
STA PT2
ISZ MVE
LDA MVE I
STA CTR
ISZ MVE
LDA PT1 I
STA PT2 I
ISZ PT1
ISZ PT2
ISZ CTR
BUN LOP
BUN MVE I
--
--
--
/ Main program
/ Branch to subroutine
/ 1st address of source data
/ 1st address of destination data
/ Number of items to move
/ Subroutine MVE
/ Bring address of source
/ Store in 1st pointer
/ Increment return address
/ Bring address of destination
/ Store in 2nd pointer
/ Increment return address
/ Bring number of items
/ Store in counter
/ Increment return address
/ Load source item
/ Store in destination
/ Increment source pointer
/ Increment destination pointer
/ Increment counter
/ Repeat 16 times
/ Return to main program
MVE,
LOP,
PT1,
PT2,
CTR,
Fortran subroutine
SUBROUTINE MVE (SOURCE, DEST, N)
DIMENSION SOURCE(N), DEST(N)
DO 20 I = 1, N
DEST(I) = SOURCE(I)
RETURN
END
20
Subroutines

## Slide 8: INPUT OUTPUT PROGRAM
Program to Input one Character(Byte)
SKI
BUN CIF
INP
OUT
STA CHR
HLT
--
/ Check input flag
/ Flag=0, branch to check again
/ Flag=1, input character
/ Display to ensure correctness
/ Store character
/ Store character here
CIF,
CHR,
LDA CHR
SKO
BUN COF
OUT
HLT
HEX 0057
/ Load character into AC
/ Check output flag
/ Flag=0, branch to check again
/ Flag=1, output character
/ Character is "W"
COF,
CHR,
Input Output Program
Program to Output a Character

## Slide 9: CHARACTER MANIPULATION
--
SKI
BUN FST
INP
OUT
BSA SH4
BSA SH4
SKI
BUN SCD
INP
OUT
BUN IN2 I
/ Subroutine entry
/ Input 1st character
/ Logical Shift left 4 bits
/ 4 more bits
/ Input 2nd character
/ Return
IN2,
FST,
SCD,
Subroutine to Input 2 Characters and pack into a word
Input Output Program